Network Basics /
Home Networking Part 1
Dave Soergel

---
Ethernet Connection
Classical Topology
MAC (Media Access Control)
  - MAC Address
    - 6 Octets (8 bit numbers)
      - e.g. 00:14:22:c8:cd:20
    - Unique
    - Sometimes settable
    - Special addresses for Multicast / Broadcast
[Speaker Notes: Show Thinnet segment]

---
Ethernet Packet
Destination
MAC Address
Source
MAC Address
Length
/ Type
       DATA
 CRC
[Speaker Notes: Break Data into chunks. Preamble Length /Type Ethernet II, IEEE 802.2/3 1500 Other possible management data CRC]

---
Hubs / Switches
Hub / Switch
Classical Hub (Multi-port Repeater)
  - Repeat packets received on one port to all the other ports.
Electronic Switch (Switch)
  - Keeps track of which MAC address is on which port and relays packets to the proper port.

---
Twisted Pair Ethernet
RJ45 Connector
Maximum length with Cat5e cable is 100 meters (~300 feet) including patch cables

---
Ethernet RJ45 Wiring

---
OSI 7 Layer Model
Image courtesy of The Abdus Salam International Centre for Theoretical Physics

---
TCP/IP
Transmission Control Protocol over Internet Protocol
The protocol suite used for the Internet
May be used over a variety of physical media (e.g. dialup, serial point to point, Ethernet)
When used over Ethernet, the IP packets are encapsulated in the “data” portion of the Ethernet packet

---
IP Address
IP address
  - (Ipv4) 4 octets of the form 192.168.1.1
  - Must be unique in your view of the network
  - Static
    - Assigned by the host's configuration mechanism.
  - Dynamic
    - Assigned by external server, typically DHCP (Dynamic Host Configuration Protocol)
    - On Ethernet, DHCP server cache associates the IP address with MAC address
    - Lease must be renewed periodically

---
TCP/IP Concepts
Ports
  - “Extension” of the address to / from a process or application on the specified IP destination
  - Of the form 192.168.1.1:80
Major Protocols: TCP, UDP
  - TCP (Transmission Control Protocol) – Connection oriented
  - UDP (User Datagram Protocol) – “Connectionless”

---
IP Routing
Subnets
  - Divide the network into independent “segments”
  - Subnet Mask indicates which piece of the IP address defines the subnet.
  - e.g. 255.255.255.0 means x.x.x.0 to x.x.x.255 are on the same subnet.
Routing
  - Transferring packets from one subnet to another that is “closer” to their destination
Gateway
  - IP Router that provides the best path to the specified destination.

---
NAT
NAT – Network Address Translation
  - Allows an IP subnet to appear as one single IP address of a parent network
  - Isolates the activity on the “private” subnet from the parent network. Only allow selected transactions to pass.
  - Should choose a reserved, non-routed private IP address range
  - Private network hosts/ports are mapped to ports on the public IP address

---
DNS
DNS (Domain Name System)
  - Allows translation of URL (Uniform Resource Locator) names to IP addresses
  - Requires specification of one or more DNS servers
  - Dynamically addressed hosts may register a name with the local DNS server

---
Simple Wired Home Network
VOIP Phone
Cable /
DSL /
Fiber
Modem
Router
Switch
Printer
PC
PC

---
Home Network Guidelines
Only one active Router
Enable NAT
Only one active DHCP Server
VOIP Phones as close as possible (fewest devices away) to the ISP modem device
Printers and servers should be Static Addresses

---
Tools
ifconfig
  - View / set interface characteristics
ping
  - Send IP packet to a host and check for reply
tracert
  - Get information on routers that packet passes through